## Slide 1: CALVIN Fall 2024 Workshop
Mustafa Dogan
November 15-18, 2024
msdogan@ucdavis.edu
GitHub repo: https://github.com/msdogan/CALVIN-shortcourse

## Slide 2: California’s water system
California has an extensive intertied water supply system
Supply-demand mismatch (spatiotemporal)
Water is mostly available in northern CA and Sierras
Agricultural demand in the Central Valley
Urban and industrial demands in the Bay area and southern CA
Reservoirs and canals were built to meet these demands in time and space

## Slide 3: Water demand
Agricultural water demand mostly in the Central Valley
Urban demand mostly in the Bay area and southern CA
Environmental demands
  Wildlife refuge
  Minimum instream flow
  Required Delta outflow

## Slide 4: Ag and urban demands
Aggregated demand areas
In CA, 70% of water is used by ag and 30% for urban
Urban demand
  Interior house
  Exterior house
  Industrial
Urban demand
Agricultural demand

## Slide 5: Environmental demand
Wildlife refuge demands
Aggregated demand areas
Mainly surface diversions
Minimum instream flow requirements
Required Delta outflow
Gray Lodge NWR
Sacramento NWR
Sutter NWR
San Joaquin West NWR and WMA
San Joaquin East NWR and WMA
Mendota WMA
Pixley NWR
Kern NWR

## Slide 6: Main surface water sources
CA’s main surface water sources:
  Trinity River (exports)
  Sacramento River
    Feather River
    Yuba River
    American River
  San Joaquin River
    Calaveras River
    Tuolumne River
    Merced River
  Kings & Kern Rivers
  Colorado River (exports)
Trinity River
Sacramento River
San Joaquin River
Colorado River
Kings & Kern Rivers

## Slide 7: Major surface reservoirs
Store water to meet urban, agricultural and environmental demands
Provide flood control
Generate hydropower
Provide recreational space
Trinity Lake
Shasta
Oroville
N. Bullards Bar
Folsom
N. Melones
N. Don Pedro
Millerton
San Luis

## Slide 8: Main groundwater sources
Central Valley aquifer (big)
  21 subbasins
Southern California subbasins (small)
Some urban communities depend solely on groundwater
Major buffer in drought years for agricultural users
Central Valley Aquifer
Groundwater subbasin

## Slide 9: Nonconventional sources
On-site reuse (agricultural)
Wastewater treatment (nonpotable)
Desalination
High cost of treatment (nonpotable and desalination)
Wastewater treatment plant

## Slide 10: Water conveyance
Mainly for urban water supply:
  California Aqueduct
  Mokelumne Aqueduct
  Hetch Hetchy Aqueduct
  Los Angeles Aqueduct
  Colorado R. Aqueduct
Mainly for agricultural water supply:
  Delta Mendota Canal
  Tehama Colusa Canal
  Friant-Kern Canal
  All American Canal
Tehama-Colusa Canal
Mokelumne Aqueduct
Hetch Hetchy Aqueduct
California Aqueduct
Delta-Mendota Canal
LA Aqueduct
Colorado R. Aqueduct
All American Canal
Clear Creek Tunnel
Friant-Kern Canal

## Slide 11: Management issues
Water demand > water supply
Worsened by nonstationary climate and frequent droughts
Environmental issues, endangered species
Aging water system (mostly built 1920-1950)
Groundwater overdraft
  Declining gw levels
  Land subsidence
  High pumping costs
  Unsustainable use of resources
  SGMA (2014) to restore gw

## Slide 12: Water management
Given water supply instruments (surface reservoirs, canals, aqueducts, groundwater pumping, water treatment etc.)
Given water demands (agricultural, urban and environmental)
Given management issues
How to better manage California’s extensive water supply system?
How to efficiently allocate limited water among different users?

## Slide 13: Hydroeconomic modeling
Combines water resources systems & economics
Allocates water among different users
Water allocations are driven by economic value of water
Economic costs & benefits are constrained by hydrology (water availability) & policies

## Slide 14: Hydroeconomic modeling
Useful for
Represents regional scale hydrologic, engineering and economic aspects
Provide a framework for water resources systems
Solution-oriented tools for discovering new strategies
Investigates water management schemes and policy insights
Useful for water resources planning & management decisions

## Slide 15: Components
Hydroeconomic models represent all major hydrologic and engineering parts of the system
Water balance components
  River flows, evaporation, groundwater recharge, and return flows
Infrastructure components
  Canals, reservoirs, treatment plants, surface and ground water pumping, and artificial recharge
Water demands (agricultural, urban, and environmental), operating costs, and operating rules

## Slide 16: Why an economical approach?
Water is a scarce source
  Should be managed and allocated efficiently
  Economics offers methods to evaluate equity and efficiency
Water has a value as a:
  Commodity in various production processes
  Diluter and transporter of waste
  Recreational space
  Ecological habitat

## Slide 17: Economic Value of water
Demand Function
Unit Price of Water ($/AF)
Market Value
Cost (or Penalty) K$
Delivery (TAF/month)
Target Delivery
Actual Delivery
Scarcity Cost
Scarcity
Strictly piecewise linear convex curves guarantee global optimum

## Slide 18: Formulation and design
Hydro-economic models use simulation and optimization separately or together.
  Simulation (What if?)
    Simulate decisions on a time-step
    Based on operating rules
    More detailed
  Optimization (What is best?)
    Objective function (minimize costs, maximize benefits)
    Physical and management constraints
    More generic
Chart: Variable
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
Simulation | 12 | 23 | 32 | 39 | 44 | 47 | 48 | 47 | 44 | 39 | 32 | 23 | 12
Optimization | 48

## Slide 19: Applications
Infrastructure planning and operation
Capacity expansion
Conjunctive use management (surface and ground water)
Water allocation and market
Adaptation (climate change)
Collaboration for conflict resolution
Design of institutional policies (water rights, flow requirements, no groundwater overdraft)

## Slide 20: Limitations
Simplification and aggregation of physical, economic and regulatory processes and data
Deterministic approach (good future knowledge)
Linearization of non-linear functions
Ideal water market operations
Mathematical representation of social, environmental and political objectives

## Slide 21: Overall
Hydro-economic models:
Represent engineered system, considering the economics of water demands and costs
Provide a framework for planning and operation
Increase system efficiency
Help decision-makers better operate complex water systems

## Slide 22: CALVIN model
CALVIN = CAlifornia Value Integrated Network
Hydroeconomic optimization model
Economics driven water allocation operations
Optimizes deliveries to users (minimizing total operating and scarcity costs)
Represents California’s water infrastructure
Historical monthly hydrology to represent hydrologic variability (Oct. 1921 to Sep. 2003)
2050 urban and agricultural demands

## Slide 23: An integrated model
CALVIN is an integrated model
Surface water & groundwater resources are used conjunctively
Aggregated environmental, agricultural & urban demands are represented
The physical system is connected via rivers, canals, aqueducts, & reservoirs
Reservoirs carry water across time-steps (multi-period model)

## Slide 24: Model coverage
Most agricultural activities & urban population (~90%)
35 agricultural & 30 urban demand locations
9 wildlife refuge demands & 21 MIF requirements
33 groundwater basins, 53 surface reservoirs

## Slide 25: Documentation
Also theses, dissertations and publications
Appendix A | SWAP Model, Agricultural Water Values
Appendix B1 | Urban Water Values I
Appendix B2 | Urban Water Values II
Appendix C | HEC-PRM
Appendix F | Environmental Constraints
Appendix G | Operating Costs
Appendix H | Infrastructure
Appendix I | Surface Water Hydrology
Appendix J | Groundwater Hydrology
Appendix K | Irrigation Water Requirements
More information and documentation about CALVIN can be found at http://calvin.ucdavis.edu/ | 

## Slide 26: Motivation for CALVIN
Interconnected water system
Integrated water management tools
  Reservoir operations
  Groundwater and conjunctive use
  Water conservation
  Wastewater reuse
  Water markets and transfers
Can we make better sense of this integrated system?
How could system management be improved?
What is system’s reaction to changes in facilities and policies?

## Slide 27: CALVIN studies
CALVIN has been used in numerous studies:
Climate change & adaptation
Groundwater overdraft
Groundwater recharge
Effects of removing a dam
Marginal value of expanding reservoir storage
Marginal value of adding/expanding infrastructure

## Slide 28: Model Components
Water sources
  Rim inflows, groundwater inflows and local runoff
Demand locations
  Agricultural, urban, and wildlife refuge
Conveyance infrastructure
  Reservoirs, pumping facilities, and canals
Capacity constraints
Regulatory requirements
  Minimum in-stream flow requirements
City A
City B
Agriculture
Aquifer
River

## Slide 29: Hydrology
RIM INFLOWS (CalSim II)
NET RESERVOIR EVAPORATION (CalSim II)
LOCAL ACCRETIONS/ DEPLETIONS (CalSim II)
GW INFLOWS (C2VSim)
SEEPAGE/ EVAPORATION LOSSES

## Slide 30: Data overflow
Water operations are driven by economic value of water: Hydrologic data + economic data

## Slide 31: Economic value of water
Monthly varying total cost curves derive operations for agricultural & urban deliveries & hydropower
Whenever a user’s total demand (target delivery) is not met, scarcity occurs
The difference between target & actual deliveries = scarcity
The scarcity cost (penalty) is total loss due to lack of water related activities

## Slide 32: Demand curves
Agricultural demand in different seasons
More flexibility (smaller slopes)
Less flexibility (steeper slopes)

## Slide 33: Agricultural demand
Chart: CVPM02G June Shortage Penalty Curve
| 25.180000305175781 | 27.690000534057617 | 30.209999084472656 | 32.729999542236328 | 35.25 | 37.770000457763672 | 40.279998779296875 | 42.799999237060547 | 45.319999694824219 | 47.840000152587891 | 50.349998474121094
 | 15219.2197 | 10709.7305 | 6785.25 | 4008.3899 | 2593.1899 | 1732.04 | 943.82 | 398.94 | 154.92 | 47.71 | 0
CVPM 1-21 in the Central Valley
Southern California demand locations
SWAP model is used to create penalty curves

## Slide 34: Agricultural demand
Two supply sources: groundwater & surface
Aggregated demand is divided into two parts based on return flow to groundwater or surface water

## Slide 35: Urban demand
Interior & exterior residential, & industrial demands
Water sources:
  Surface water
  Groundwater
  Desalination
  Potable & non-potable recycled water

## Slide 36: Wildlife refuge demand
9 wildlife refuge demand locations
No economic representation
Constrained water deliveries
Supply sources:
  Surface water
  Groundwater
  Agricultural return flow

## Slide 37: MIF Requirements
Minimum in-stream flow requirements due to aquatic habitat needs
Represented as lower bound constraints
Time-series obtained from CALSIM III model

## Slide 38: Hydropower
Monthly hydropower operations
Penalty for not generating hydropower (reverse of a benefit curve)
Represented on reservoir storage and release
Hourly average energy prices
Chart: Shasta Linear Hydropower Penalty Surface for July
| 0 | 239.13864042193256 | 358.70796063289885 | 478.27728084386513 | 597.84660105483135 | 717.41592126579769 | 836.98524147676403 | 956.55456168773026 | 1076.1238818986965 | 1195.6932021096627
116 | 9292.7617 | 9132.3786 | 9054.9572 | 8978.3682 | 8902.9328 | 8829.0652 | 8758.9324 | 8704.5557 | 8700.8857 | 8700.8857
851 | 6270.4448 | 6110.0617 | 6032.6403 | 5956.0513 | 5880.6159 | 5806.7483 | 5736.6156 | 5682.2388 | 5678.5688 | 5678.5688
2747 | 4015.2018 | 3854.8188 | 3777.3974 | 3700.8084 | 3625.3729 | 3551.5053 | 3481.3726 | 3426.9959 | 3423.3259 | 3423.3259
4302 | 2518.5228 | 2358.1397 | 2280.7183 | 2204.1293 | 2128.6939 | 2054.8263 | 1984.6936 | 1930.3168 | 1926.6469 | 1926.6469

## Slide 39: CALVIN limitations
CALVIN has several limitations:
Perfect hydrologic knowledge (limited in limited foresight model)
Simplified groundwater representation (unit fixed pumping cost)
Linearized cost curves (piecewise linear)
Simplified hydropower representation due to linear programming (LP) framework

## Slide 40: Lessons from CALVIN
CALVIN results show that
Regional or statewide markets can reduce water scarcity costs
Environmental flows have economic values for agricultural and urban and hydropower activities
Economic values exist for expanded facilities
Some scarcity is optimal
Integrated local, regional, and statewide operation of water decreases competition with environmental uses (water trading)

## Slide 41: CALVIN goals
The recent updates aims to
Create a cross-platform model: MacOS, Windows
Use open data format: csv, JSON
Have freely available: data, code, modeling language & solvers are open-source or free of charge
Separate model & data:
  HOBBES is independent from any data
  CALVIN’s structure code is generalized (can solve any other network-flow problems)

## Slide 42: CALVIN improvements
The original CALVIN uses HEC-PRM to solve its optimization problem
With recent updates, CALVIN is moved to Python
Pyomo library, a high level optimization modeling language in Python, is used
Pyomo can connect to several freely available solvers
Runtime is decreased from 2-5 days to 30min-1 hr, with parallelization in Pyomo.

## Slide 43: HOBBES database
A web-based open-source data storing and sharing platform
Stores California’s water network data
Documentation and change tracking via GitHub
Data visualization and animation
Several models can be built around HOBBES, where built-in tools convert and export network data in the desired format
HOBBES
Database
CALVIN
HEC-PRM
CALVIN
Python version
Water-Energy
network-flow
Other models
...
https://cwn.cws.ucdavis.edu

## Slide 44: HOBBES visualization
California water network
Geocoded network elements
Layered based on hydrologic regions and subregions
Data visualization
Animation tool
https://cwn.cws.ucdavis.edu

## Slide 45: HOBBES for CALVIN (Python)
CALVIN Python version uses matrices for all parameters: c, a, l, u
Calvin-network-tool in HOBBES converts input data into a network matrix
The network matrix is input to CALVIN (Python)
Each of network matrix lines correspond to a link – decision var. (full size model has 6 millions)
i | j | k | c | a | l | u

## Slide 46: Network-flow model
CALVIN represents the physical system with nodes and links
Nodes represent reservoirs, demand locations, power and pumping plants and junctions
Links only connect nodes to each other
All network parameters are applied to links: amplitude (loss factor) a, unit cost c, lower bound l, & upper bound u

## Slide 47: Linear Programming model
As an network-flow LP model, CALVIN minimizes statewide water scarcity and operating costs within constraints
 | Objective Function
 | Lower bound constraint
 | Upper bound constraint
 | Mass balance constraint
 | Objective Function
 | Lower bound constraint
 | Upper bound constraint
 | Mass balance constraint
where X is flow (decision variable); c is unit cost; l is lower bound; u is upper bound; a is amplitude
index i represents origin node; j is terminal node; k is a piecewise component

## Slide 48: Resolving infeasibilities
When a mass-balance constraint at any location is not met, the model results in infeasible solution
Due to size of the model, in case of infeasibility, you never know where the problem is
Flow =
100 TAF
Flow =
500 TAF
Capacity =
550 TAF
Flow =
100 TAF
Flow =
500 TAF
Lower Bound =
650 TAF

## Slide 49: Debug mode
When network is modified (climate change, adding a new requirement or element etc.), first run in debug mode
Debug mode adds two links (debug source & debug sink) at very high cost (~1010)
The debug cost is much higher than any other cost in CALVIN to make sure it is not used unless there is infeasibility
Then postprocess to
eliminate debug flow
c = $1010
c = $1010

## Slide 50: CALVIN runtime
Solver wall clock runtime for different model sizes
Installed solvers:
  GLPK
  CBC
  Gurobi
  CPLEX
Log-log scale: exponential increase of runtime

## Slide 51: Recent hydrology updates
1st generation CALVIN: 1921-1993 (72 years)
2nd generation CALVIN: 1921-2003 (82 years)
3rd generation CALVIN: 1921-2015 (94 years)
The more period, the more floods and droughts, the better system representation
Input hydrology
  2nd generation: CALSIM II model
  3rd generation (updated): CALSIM III model

## Slide 52: Updated components
Rim inflows
Groundwater inflows
Local inflows
Reservoir evaporation
Environmental demand
  Min. instream flow req.
  Req. Delta outflow
  Wildlife refuge demands
SJR at Vernalis minimum instream flow requirements
Shasta Lake reservoir evaporation rate
Sacramento River at Shasta unimpaired rim inflow
Groundwater subbasin-4 net monthly recharge

## Slide 53: Comparing V2 and V3 CALVIN
Agricultural scarcities increase in drought years
On average, less scarcity in updated CALVIN
Drought years

## Slide 54: Comparing V2 and V3 CALVIN
Surface storage variability slightly increase
Mean storage remains the same
mean storage
50% of time

## Slide 55: Comparing V2 and V3 CALVIN
Delta exports (CAA & DMC)
Banks PP allowable pumping capacity (reduced)
Surplus Delta outflow decrease
mean export
50% of time
Wet years

## Slide 56: Remaining updates/issues
Demand curve updates (agricultural and urban)
Improving data quality for groundwater inflows
Graphical user interface
Network modification documentation
Generic postprocessors to organize and visualize CALVIN outputs

## Slide 57: A small network example
Modeling of a reservoir with following properties
Two time-steps

## Slide 58: Network-flow form