## Slide 1: Spring 2017 PyVIN Shortcourse & Hands-on Tutorial
Mustafa Dogan
Center for Watershed Sciences, UC Davis
Spring 2017

## Slide 2: Agenda
CALVIN theory & model introduction
  break
HOBBES database
Data flow overview
  Break (lunch)
PyVIN updates & model architecture
  break
First PyVIN run
Postprocessing results

## Slide 3: CALVIN Theory & Model Introduction

## Slide 4: CALifornia Value Integrated Network
Hydroeconomic optimization model
Represents California’s water operations
Optimizes water deliveries to users
Surface and groundwater representation
Historical monthly hydrology (from Oct 1921 to Sep 2003)
2050 agricultural and urban demands

## Slide 5: Water Allocation
Economic values for agricultural, urban and hydropower uses
Constraints for capacity limitations and regulatory requirements
82-year hydrology and operations
Monthly time-step
City A
City B
Agriculture
Basin
Aquifer
River
$
$
$
$

## Slide 6: CALVIN
Forces quantitative understanding of integrated water and economic system
Optimization tools from engineering
Ideas from economics
Provides insights into regional and statewide water planning and management

## Slide 7: Motivation
Make better sense of integrated system and operations
Seek ways to improve system management
Quantifying user willingness to pay for additional water
Find insights into changes in physical capacities and policies

## Slide 8: Model Coverage
Most agricultural activities and urban population
Major conveyance systems (CAA, DMC, CRA)
CVP and SWP operations
Surface and groundwater reservoirs

## Slide 9: Network-Flow Structure
Nodes
  Reservoirs, plants, demand areas
Links
  Capacity (upper bound), minimum flow (lower bound), loss (amplitude), cost
CALVIN network schematic
i
j
origin
node
terminal
node
link
link

## Slide 10: Water Users: Demand Areas
Users
  Agricultural
  Urban
  Environmental
Economic representation for ag and urban
  Penalty for not delivering water
  Urban users with higher WTP
Constrained (fixed) deliveries for environment (wildlife refuges)
Chart: Agricultural Shortage Penalty (CVPM13G - may)
| 136.8500061035156 | 150.529998779297 | 164.2200012207031 | 177.8999938964844 | 191.5899963378906 | 205.2700042724609 | 218.9600067138672 | 232.6399993896484 | 246.3300018310547 | 260.0100097656249 | 273.7000122070312
 | 73060.6172 | 57403.4102 | 45090.6289 | 35526.5 | 26739.3691 | 18543.5508 | 11191.5195 | 6125.73 | 3262.3899 | 1012.86 | 0
Chart: Urban Shortage Penalty (EBMUD ext - june)
| 1.289999961853027 | 3.859999895095824 | 6.429999828338623 | 9.010000228881835 | 10.28999996185303 | 11.57999992370605 | 12.22000026702881 | 12.86999988555908
 | 561962.1875 | 66161.6328 | 20769.3008 | 7438.8799 | 4065.95 | 1711.38 | 791.4 | 0

## Slide 11: Demand Area Penalty Curves
Penalty for not delivering water (and economic loss)
No penalty at the target delivery
Piecewise linear curves (linear programming model)
User’s willingness to pay (WTP) for water
Convex: the more delivery the less penalty
Chart: Delivery (TAF)
| 136.8500061035156 | 150.529998779297 | 164.2200012207031 | 177.8999938964844 | 191.5899963378906 | 205.2700042724609 | 218.9600067138672 | 232.6399993896484 | 246.3300018310547 | 260.0100097656248 | 273.7000122070312
 | 73060.6172 | 57403.4102 | 45090.6289 | 35526.5 | 26739.3691 | 18543.5508 | 11191.5195 | 6125.73 | 3262.3899 | 1012.86 | 0
Actual delivery
Actual penalty
Target
delivery
Scarcity
Marginal WTP for additional water ($/AF)

## Slide 12: Monthly Varying Demand Curves
Demand curves vary by month (no annual variation)
Higher target demand in summer months
Less price elasticity (steeper slope) in winter months

## Slide 13: Agricultural Representation
SWAP Model Coverage
Results from Statewide Agricultural Production (SWAP) model
SWAP simulates farmers decision in California
Profit maximization model
35 aggregated subbasins
SWAP results are used to create ag penalties in CALVIN (& PyVIN)
Production
Water
Labor

## Slide 14: Agricultural Demand
Supply sources:
  Groundwater
  Surface water
Split into two parts depending on return flows
groundwater
surface water
HGP
A
SW u/s
HGR
α, $
Pumping Capacity
Pumping Cost
A < 1
Conveyance Loss
A<1
% GW Return Flow
GW
HSU
α, $
Conveyance Capacity
Distribution Cost
HU
gw return
HSD
A<1
% SW Return Flow
A > 1
Ag Reuse
α=UBT, $=TD
Target Delivery
Shortage Penalty
α=UBT, $=TD
Target Delivery
Shortage Penalty
SW d/s
surface return

## Slide 15: Urban Demand
HGP
U
WTP
SW u/s
industrial
exterior
interior
WWP
GW
HGR
HNP
α=UBC, $
Pumping capacity
Pumping cost
A<1
Industrial Urban
Use Return Flow
A<1
Interior Urban
Use Return Flow
$
Treatment Cost for discharge into GW basin
α=UBC, $
WWTP capacity
for non-potable use
Treatment Cost
α=UBT, $=TD
Target Delivery Shortage Penalty
A<1
Exterior Urban
Use Return Flow
Aggregation Node
α=N/A, $
WTP capacity
Treatment cost
α=UBC, $
Canal capacity
Distribution Cost
α=UBT, $=TD
Target Delivery Shortage Penalty
α=UBT, $=TD
Target Delivery Shortage Penalty
α=UBC, $
WWTP capacity
for potable use
Treatment Cost
$
Treatment Cost for discharge into SW source
SW d/s
HP
Desalination
HXI
Supply sources:
  Groundwater
  Surface water
Split into three parts
  Exterior
  Interior
  Industrial

## Slide 16: Wildlife Refuge Demand
Wildlife Refuge
R###
HSUR###
HSR###
HSD###
GW ##
HGP##
d/s
α
Diversion Capacity
α, $
Pumping Capacity & Cost
α
Ag Return Flow Diversion Capacity
A>1
Reuse Capability
A<1
Return Flow
α=EQC
Refuge Target Demand
HSU###
A<1
Conveyance Losses
groundwater
surface water
ag return flow
Supply sources:
  Groundwater
  Surface water
  Ag return flow
Constrained (fixed) flow deliveries

## Slide 17
Advantages
Integrated model (surface and groundwater)
Unique combination of economics and engineering principles
Well-documented model (reports, articles, website and theses)
Limitations
Perfect hydrologic foresight
  The model knows all hydrologic events in its operating period
  Scarcity costs are less than actual
Simplified reservoir and Delta operations
Piecewise linearization
Simplified hydropower representation

## Slide 18: HOBBES Database

## Slide 19: HOBBES
A bottom up approach to improve and organize data
Venue for modelers to create an open, organized and documented water representation
Geocoded elements can be converted to networks and solved by multiple modeling platforms (PyVIN)

## Slide 20: Modeling with HOBBES
HOBBES
CALVIN
PyVIN
Other Models
Online Database
Version Control
Data Visualization
Documentation
Collaboration
model
model
data
model
1
model
data
data
Classical Approach
1
2
2
2
3

## Slide 21: HOBBES Website
California water network
Geocoded network elements
Layered based on hydrologic regions and subregions
Data visualization
Animation tool
https://cwn.casil.ucdavis.edu

## Slide 22: Data Visualization
Graph flow and storage results
Select time-period
Animation tool
Inflow, flow, storage, evaporation

## Slide 23: Data Flow Overview

## Slide 24: Hydrology
RIM INFLOWS (CalSim II)
NET RESERVOIR EVAPORATION (CalSim II)
LOCAL ACCRETIONS/ DEPLETIONS (CalSim II)
GW INFLOWS (C2VSim)
SEEPAGE/ EVAPORATION LOSSES
Image: California Water Plan Update 2013

## Slide 25: Operating Cost
WATER TREATMENT COST
HYDROPOWER BENEFITS
ARTIFICIAL RECHARGE OPERATION COST
PUMPING COST
Image: California Water Plan Update 2013

## Slide 26: PyVIN Model

## Slide 27: Goals
data transparency
collaboration
run speed
version control
documentation

## Slide 28: CALVIN
HOBBES Database
~1250 nodes
~600 conveyance links
49 surface reservoirs
38 groundwater reservoirs
88% of CA’s irrigated acreage
92% of CA’s urban population
https://cwn.casil.ucdavis.edu

## Slide 29: Modeling Environment
Pyomo is a Python-based, open-source optimization modeling language
Algebraic language similar to GAMS, AMPL
Easy to install: ”conda install -c cachemeorg pyomo”
User defined solvers:
  CPLEX1
  GUROBI1
  CBC2
  GLPK2
http://www.pyomo.org/documentation
(1 free for academic purposes only, 2 open source)

## Slide 30
CALVIN v.1 | PyVIN v.2
Large-scale hydroeconomic model | 
Optimize water allocation to agricultural and urban users | 
Minimize statewide water scarcity and operating costs | 
HEC-PRM and VBA based | Pyomo and Python based
Less flexible (limited to HEC-PRM) | More flexible (full LP)
Solver runtime: ~16 hr (depending on initial solution) | Solver runtime: ~1 min (depending on solver)
Requires 32 bit Windows PC | Any computer
HEC-DSS database | Open source: data and source code

## Slide 31: HOBBES Matrix Creator
Calvin (2014)
Calvin (2015)
Errata (2014-2015)
Calvin (2015)
Calvin (2015)
extra
Calvin (2015)
Calvin (2015)
Calvin (2015)
Calvin (2015)
Calvin (2015)
Calvin (2015)
Calvin (2015)
+
Q* (objective)
Price ($/Vol)
Q (volume)
p*
Demand Curves
Time-series
Data Matrix (PyVIN input)
hydrograph

## Slide 32: PyVIN Model Structure
Freely Available Solvers
3
CPLEX
CBC
GUROBI
GLPK
User installed and defined solvers
No dependency on any solver
Abstract Model in Pyomo
Model Structure
Data
PyVIN
2
Separate data and model structure
where
Z: total cost
X: flow on the arc
c: unit cost (or penalty)
b: external flow
a: amplitude
l: lower bound
u: upper bound
objective
mass balance
Linear Programming Model with Gains & Losses
1
upper bound
lower bound

## Slide 33: PyVIN Run Process
HOBBES
Input Data
Network matrix
Pyomo
Model Run
Specify data file and solver
Python
Postprocess Results
Analyze results stored in *.csv files
HOBBES
Data Visualization
Time-series plots & animation

## Slide 34: PyVIN
Output
Input
pyvin.py
data.dat
flow.csv
storage.csv
shortage cost.csv
dual - lower bound.csv
dual - upper bound.csv
benefits of capacity expansion
water deliveries to users
surface and groundwater storage
cost of shortage to users and WTP for additional water
shadow prices of environmental flows

## Slide 35: Solver Time
Runs are performed on UC Davis College of Engineering’s HPC1 (High Performance Computer)
cbc, cplex and gurobi are run in parallel, and glpk is run in serial
number of decision variables
time (second)
~35K
~1.4M
~3M
open source
glpk
Y=(9.83E-10)X2.19551
cbc
Y=(5.59E-09)X1.83019
gurobi
Y=(3.77E-08)X1.52444
cplex
Y=(7.84E-08)X1.41141

## Slide 36: Total Runtime
time (second)
number of decision variables
Differences get bigger as model size increases
cplex and gurobi have similar total runtime
# of decision variables | output file size (json)
35,827 | ~7.5 MB
1,430,915 | ~300 MB
2,933,335 | ~602 MB
~35K
~1.4M
~3M
Pyomo builds the model
Solver finds a solution
Pyomo writes results
glpk
Y=(2.88E-08)X1.96947
cbc
Y=(3.11E-05)X1.27684
gurobi
Y=(4.13E-04)X1.02861
cplex
Y=(3.46E-04)X1.03667

## Slide 37: Solver Accuracy
Objective value normalized to glpk results
cbc results slightly lower
Overall consistent solver results
Normalized to glpk (%)
Chart: 
| 2.933335E6
glpk | 100
cbc | 100
cplex | 100
gurobi | 100
Chart: 
| 1.430915E6
glpk | 100
cbc | 100
cplex | 100
gurobi | 100
glpk
cbc
cplex
gurobi
Chart: 
| 35827.0
glpk | 100
cbc | 100
cplex | 100
gurobi | 100
glpk
cbc
cplex
gurobi
glpk
cbc
cplex
gurobi
~35K
~1.4M
~3M
solvers
model size
Solver Result Comparison

## Slide 38: Preliminary Results
Lower Sacramento
& Delta
Monthly Change in Overall Storage (MAF)
Oct-1921
Sep-2003
ΔSurface water
Sep-2003
ΔGroundwater
Oct-1921
Monthly Avg. Delivery (TAF/m)
Upper Sacramento
San Joaquin
& South Bay
Tulare Basin
Southern California
Groundwater
Surface water
Agricultural Delivery
Urban Delivery

## Slide 39: Limitations & Improvements
Perfect foresight
  Run year-by-year to prevent perfect hydrologic foresight
Groundwater representation
  Implement SGMA constraints on groundwater basins
Water rights
  Represent water rights in system operations

## Slide 40: Software Installation & Your 1st PyVIN run

## Slide 43: Postprocessing Results